## Slide 1
Ensuring Plastic Additives used in Sensitive Applications are Fit for Use
2019 SPE International Polyolefins Conference
David Horst, BASF Corporation
Dr. Tobias Eltze, BASF SE
February 27, 2019
Houston, TX

## Slide 2: Fitness for Use in Sensitive Applications
Quality System
Mgt. responsibility
Management of Change
CA & PA
Traceability
Quality risk analysis
External NIAS Control
Supply chain comm.
Degradation/ reaction prods
Downstream processes
Product Listing
Data generation
Analytical work
Migration testing
Application areas
Internal NIAS Control
Hazard assessment
Exposure assessment
Risk assessment
Specifications
Suitable Purity
Fitness for Use
Regulatory Compliance
Sustainability
Product Defense  Communication
Associations  Authorities
Other Stakeholders
Notes: Product must conform to the characteristics of the approved product.
Market/ external: Communication in the supply chain – both ways.
Associations working with global authorities
Public or authorities – have been known to identify NIAS.

## Slide 3: Sensitive Applications for Plastic Additive Products
Antioxidants
Process stabilizers
UV absorbers
Light stabilizers
Clarifying agents
Nucleating agents
Antistatic agents
Slip agents
Acid neutralizers
Visbreakers
Notes: We both support the BASF Plastic Additives business. Our business is a global one which encompasses approximately 15 production and blending sites throughout the world. These sites serve their regions but also the global market either via direct sales or via our customers’ supply chains. We either supply or utilize in blends the following additives. They go into many types of applications including food packaging and water pipe as well as pharma packaging and cosmetics. The majority of products in our portfolio have some compliance in sensitive applications.

## Slide 4: Why start with Food Contact?
Food Contact is a fundamental requirement for many sensitive regulations!
Food Contact
Pharma Packaging / Medical Devices
Cosmetic Packaging
Construction Products in Contact with Drinking Water
Product Safety

## Slide 5
Fitness for Use in Sensitive Applications
Quality System
Mgt. responsibility
Management of Change
CA & PA
Traceability
Quality risk analysis
External NIAS Control
Supply chain comm.
Degradation/ reaction prods
Downstream processes
Product Listing
Data generation
Analytical work
Migration testing
Application areas
Internal NIAS Control
Hazard assessment
Exposure assessment
Risk assessment
Specifications
Suitable Purity
Fitness for Use
Regulatory Compliance
Sustainability
Product Defense  Communication
Associations  Authorities
Other Stakeholders
Notes: Product must conform to the characteristics of the approved product.
Market/ external: Communication in the supply chain – both ways.
Associations working with global authorities
Public or authorities – have been known to identify NIAS.

## Slide 6: Food Regulation Compliance
Compliance with food contact regulations involves 5 aspects:
  Listing of the product on the positive list – Declaration of Compliance
  Byproducts and residuals are controlled within safe levels
  Degradation products from normal use must be assessed
  Adequate control of product purity (major requirement for shared facilities)
  Specific quality management system components
Notes: This is one of the most important, time consuming and expensive parts of bringing a new product to market. We must conduct tox testing, analytical characterization, and migration testing from different plastics into multiple food simulants
Product purity relates especially to shared facilities and possible cross contamination with other products.
Re: NIAS. We as producer have the obligation to assure the safety of components in our products but not included on the regulatory positive list
The FCCs and GMP declarations commit the company to meeting the requirements.
Customers expect BASF to be the benchmark in these aspects

## Slide 7: Definitions - GMP
21 CFR 174.5 General provisions applicable to indirect food additives | 
Good manufacturing practices [are] defined to include the following restrictions: | Quantity limited by prescribed limits, technical effect in article, no intended effect in food Any substance used as a component of articles that contact food shall be of a purity suitable for its intended use Existence of a prescribed limit does not exclude from meeting other requirements
Article 3 of EC Regulation 1935/2004 (The Framework Regulation) | 
"Materials and articles.... shall be manufactured in compliance with good manufacturing practice so that, under normal or foreseeable conditions of use, they do not transfer their constituents to food in quantities which could: | Endanger human health or bring about an unacceptable change in the composition of the food or bring about a deterioration of the organoleptic characteristics thereof
GMP: Good Manufacturing Practices
As defined by specific regulations

## Slide 8: Changes from New EU Regulations EC 2023/2007; EC 10/2011
More explicit requirements for the quality system
  Management responsibility
  Training
  Evaluation of starting materials
  Documentation
More explicit requirements for Quality Control
  Monitoring of GMP attainment
  Corrective actions for failures
NIAS are defined to include impurities, reaction intermediates from the production process and reaction or degradation products
Risk assessment in accordance with internationally recognized scientific principles

## Slide 9
Fitness for Use in Sensitive Applications
Quality System
Mgt. responsibility
Management of Change
CA & PA
Traceability
Quality risk analysis
External NIAS Control
Supply chain comm.
Degradation/ reaction prods
Downstream processes
Product Listing
Data generation
Analytical work
Migration testing
Application areas
Internal NIAS Control
Hazard assessment
Exposure assessment
Risk assessment
Specifications
Suitable Purity
Fitness for Use
Regulatory Compliance
Sustainability
Product Defense  Communication
Associations  Authorities
Other Stakeholders
Notes: Product must conform to the characteristics of the approved product.
Market/ external: Communication in the supply chain – both ways.
Associations working with global authorities
Public or authorities – have been known to identify NIAS.

## Slide 10: Good Manufacturing Practices for Additives Manufacturers
Process
Raw Materials
Solvents
Other materials
SOP
Cross contamination
Spec
MOC
MOC
Spec
params
Main Ing.
By-prod
residuals
Listing
Spec.
Analysis
Granulation
Blending
Spec
Cross contamination
~15 sites
~12 sites
Spec
Key
Spec – Specifications
MOC – Management of change process
Params - Process control parameters
Analysis – Detailed analytical fingerprint for checking effect of proposed changes
Listing – Inclusion on authorities positive list
SOP – Standard operating procedure
Common Processes
Quality Management system
Management awareness
Training
Audits
HACCP (for blending)

## Slide 11: Specifications for Cross Contamination in blending facilities
Numbers in cells represent the maximum cross contamination level in ppm of the substance in column A into the substance in Row 4 | Max Concentration in plastic (ppm), Z | AO AcidNeut blend | AO Blend 1 | AO UVA blend | AO Blend 3 | AO Blend 2 | AO-Hals blend 1 | HALS1
Max conc. for sensitive appl.(wt%) |  | 1 | 0.6 | 0.6 | 0.4 | 0.4 | 0.33 | 0
HALS1 | 0.65 |  |  |  |  |  |  | NA
AO-Hals blend 1 | 0.66 |  |  |  |  |  | NA | 
AO UVA blend | 3.12 |  |  | NA |  |  |  | 
AO Blend 2 | 529 | 1000 | 1000 | 1000 | 1000 | NA | 1000 | 
AO Blend 3 | 698 | 1000 | 1000 | 1000 | NA | 1000 | 1000 | 
AO AcidNeut blend | 2717 | NA | 1000 | 1000 | 1000 | 1000 | 1000 | 
AO Blend 1 | 3618 | 1000 | NA | 1000 | 1000 | 1000 | 1000 | 
Four Zones
and marginal areas
Zone 1
Zone 2
Zone 3
Zone 4
Sensitive into sensitive
Industrial into sensitive
Industrial into Industrial
Sensitive into Industrial
2
3
4
1
Notes: Need to take care of technical limitations on top of this.
Just show zones?
Make numbers easier to see

## Slide 12: Risk Assessment Steps: guideline developed by Food Contact Additive Sector Group of Cefic
Risk Assessment of NIAS e.g. Impurities, byproducts Reaction- and Degradation Products
Migration into food evaluation by tiered approach Worst case calculation, if not OK experimental testing needed
Toxicology assessment of migrants regarding CMR criteria and
Derive where applicable Tolerable Daily Intake (TDI) threshold or determine Threshold of Toxicological Concern (TTC)
Verify restrictions set by Authorities
Conclude on tolerable migration into food
File Risk Assessment as Supporting Document (SD)
CMR = Cancerogenic, Mutagenic, Reprotoxic
R
I
S
K

## Slide 13
Fitness for Use in Sensitive Applications
Quality System
Mgt. responsibility
Management of Change
CA & PA
Traceability
Quality risk analysis
External NIAS Control
Supply chain comm.
Degradation/ reaction prods
Downstream processes
Product Listing
Data generation
Analytical work
Migration testing
Application areas
Internal NIAS Control
Hazard assessment
Exposure assessment
Risk assessment
Specifications
Suitable Purity
Fitness for Use
Regulatory Compliance
Sustainability
Product Defense  Communication
Associations  Authorities
Other Stakeholders
Notes: Product must conform to the characteristics of the approved product.
Market/ external: Communication in the supply chain – both ways.
Associations working with global authorities
Public or authorities – have been known to identify NIAS.

## Slide 14: GMP in the Supply Chain
Synthesis
  Byproducts
  Specifications
  X-contamination
  Raw materials
Blending
  X-contamination
Masterbatch/ Compounding
  Reaction prods
  X-contamination
Conversion
  Reaction Prods
End User
  Reaction prods

## Slide 15: Degradation Products (ARVIN Substances)
Arvin 1 123-07-9 4-Ethylphenol | Arvin 2 98-54-4 p-tert-Butylphenol | Arvin 3 719-22-2 2,6-Di-tert-butyl-p-benzoquinone | Arvin 4 96-76-4 2,4-di-tert- Butylphenol | Arvin 5 52858-87-4 3,5-di-tert-butyl-4-hydroxystyrene
Arvin 6 1620-98-0 3,5-di-tert-butyl-4-hydroxybenzaldehyde | Arvin 7 14035-33-7 3,5-di-tert-butyl-4- hydroxy acetophenone | Arvin 8 82304-66-3 7,9-Di-tert-butyl-1-oxaspiro(4,5)deca-6,9-diene-2,8-dione | Arvin 9 6386-38-5 3-(3,5-di-tert-butyl-4-hydroxyphenyl) methylpropanoate | Arvin 10 20170-32-5 3-(3,5-di-tert-butyl-4-hydroxyphenyl) propanoic acid
Notes: The German national competent authority Federal Institute for Risk Assessment has identified information gaps for some substances that are the degradation products in polyolefin pipes for drinking water application. In their safety assessment, the competent authority concluded that the toxicity profile is insufficient to come up with a clear statement and more data on the genotoxicity potential of Arvin VIII should be generated. ELiSANA embarked a testing program on assessing further the toxicity profile of reaction products

## Slide 16: Types of Non-Intentionally Added Substances (by origin)
Type of NIAS | Responsibility | Control
Byproducts and Residuals | Manufacturer | Manufacturer
Cross Contamination | Manufacturer | Manufacturer
Normal reaction products | Joint | Joint
Products from downstream chemistry | End user | End user/ Joint
We are identifying the NIAS and inform our customers on NIAS, if there is a possibility that they are formed during processing in the value chain.
BASF inform customers proactively in the FCC’s since January 1, 2017 (example for Irgafos®168):

## Slide 17: Fitness for Use in Sensitive Applications
Quality System
Mgt. responsibility
Management of Change
CA & PA
Traceability
Quality risk analysis
External NIAS Control
Supply chain comm.
Degradation/ reaction prods
Downstream processes
Product Listing
Data generation
Analytical work
Migration testing
Application areas
Internal NIAS Control
Hazard assessment
Exposure assessment
Risk assessment
Specifications
Suitable Purity
Fitness for Use
Regulatory Compliance
Sustainability
Product Defense  Communication
Associations  Authorities
Other Stakeholders
Notes: Product must conform to the characteristics of the approved product.
Market/ external: Communication in the supply chain – both ways.
Associations working with global authorities
Public or authorities – have been known to identify NIAS.

## Slide 18: Challenges
Business awareness?
Capital projects coming?
People Turnover?
Inventory targets?
Changes?
Business management support? Understand?
Market requires?
Regulatory
mandates?
Notes: Could also mention positive drivers…

## Slide 19: Program approach
Management commitment
  Business management
  Production management
  Product management
Buy – in
  Regional PMs
  Site quality
  Site mgt.
Implementation
Training
Documentation
Tools
Audits
Establish Team
  Partnership with Quality Mgt
  Strong Global collaboration
  Division of responsibilities

## Slide 20: The Continuous Improvement Cycle
Plan
Do
Check
Act
Evaluate risk
Preventative controls
Targets
Procedures
Training
Document
Audit
Analyze trends
Measure
Change & evolve
Improve & learn
Reduce waste & risk

## Slide 21: Management of Change
MOC
Engagement
CCC
Training
Process
System
Notes: Transition slide
Continuous training
Value of ccc—learning and improvement

## Slide 22: Fitness for Use in Sensitive Applications
Quality System
Mgt. responsibility
Management of Change
CA & PA
Traceability
Quality risk analysis
External NIAS Control
Supply chain comm.
Degradation/ reaction prods
Downstream processes
Product Listing
Data generation
Analytical work
Migration testing
Application areas
Internal NIAS Control
Hazard assessment
Exposure assessment
Risk assessment
Specifications
Suitable Purity
Fitness for Use
Regulatory Compliance
Sustainability
Product Defense  Communication
Associations  Authorities
Other Stakeholders
Notes: Product must conform to the characteristics of the approved product.
Market/ external: Communication in the supply chain – both ways.
Associations working with global authorities
Public or authorities – have been known to identify NIAS.

## Slide 23: Degradation/ Reaction products NIAS? Resource?
Additives producers within ELiSANA recently successfully concluded genotoxity testing of numerous reaction products (AKA Arvin substances)
The drive was from the drinking water authorities
ELiSANA Membership:
Adeka Palmarole
Addivant
BASF
Oxiris
SI Group
Songwon
Arvin 3: 2,6 di tertbutylbenzoquinone
Arvin 6: 3,5 di tert butyl 4-hydroxy benzaldehyde
ELiSANA: European Light Stabilizer and Antioxidant Association

## Slide 24: Network of Support
Business
Product mgt
Leadership
Production mgt
Sales mgt
Sales Force
Brand Owner
Contract lab
Customer
Data
Tox
Analytical
petitions
Papers
Process
Procedures
Guidelines
Systems
SOPs
Standing meetings
Quality Mgt
Global head
GMP Lead
Regional leaders
Sites
Schedulers
Plant manager
QC Analytical
Unit Mgrs
Plant Engineers
Site quality
Experts
Tox
Food contact
R&D chemists
Application experts
Lawyers
Process Development
Product Steward
Functional Lead
Regional stewards

## Slide 25: Summary
Assuring Fitness for Use is complex
Not just a regulatory activity
Requires
  Management commitment/ awareness
  Team of experts
  Systems
  Data
Communication in the supply chain
Our Program is in Place and Working